## Slide 1
Colposcopic
instrumentation
and Planing colposcopy clinic
Sathone Boonlikit,MD
Assoc Prof.
Division of Gynecologic Oncology
Rajavithi Hospital , Medical College Rangsit University ,Thailand
Sep 4-5 2017
Notes: - I’ve divided my presentation into ..2 parts

## Slide 2
INSTRUMENTATIONS
OF
COLPOSCOPY

## Slide 3: Intrumentation
Colposcope
Equipment for examination
Biopsy Forceps
Additional instrument
Other equipment
Notes: Can be taken from gyn clinic
Some are special instrument that we have to provide
Obtain
Particulary provided

## Slide 4
Main objective Lens
Magnification changer
Eye pieces
Fine focus adjustment
Colposcope
Handle
Green filter
Notes: Is a medical diagnostic procedure to examine an illuminated, magnified view of the cervix and the tissues of the vagina and vulva
Component
accessory
Consist of
Composed of
an instrument for examining the uterine cervix, esp for early signs of cancer
Fine focus = move very slightly
Unlike a (monocular) telescope, binoculars give users a three-dimensional image: for nearer objects the two views, presented to each of the viewer's eyes from slightly different viewpoints, produce a merged view with an impression of depth.

## Slide 5
OBJECTIVE LENS
- focal length 250-350 mm.
- working distance
Focal point
Image
Object
Object distance
Notes: It is set from the factory. You can change to another focal length,
Fiexed focal length and wide aperture, that’s mean the picture is clear when the object is just at the focal point.
To achieve that , we have to move the instrument closer or further any we want to adjust . This focal distance refers to working distance
Because it is an available distance and space that doctors have from the cervix. Too short or too long is not good
focus is not adjustable is called a fixed-focus lens
The image is out of focus.
In case of colposcope , you could not adjust the focus of the lens, you would have to move physically closer or further from the object

## Slide 6: Equipment for examination
Speculum
Cotton-tipped applicator & cotton swabs
Packing forceps
Sponge forceps
Biopsy instrument
Solution : Acetic 3-5% / Lugol / NSS
Others

## Slide 7: Speculum
Nonrefelctive matt surface : for laser and photography
Insulated, vinyl coated : for LEEP
Tube for evacuate plume
Autoclavable
Notes: Variety sizes

## Slide 8: Biopsy Forceps
Ideally, rectangular specimen
Teeth on jaws prevent slipping during biopsy
Spring handle => better cutting
Kevorkian biopsy forceps = Rectangular
Tichler-Morgan biopsy forceps = Spring handle and teeth on both jaws

## Slide 9: Biopsy forceps

## Slide 10
SILVER NITRATE STICK
Monsel Solution
LUGOL / ACETIC A

## Slide 11: Additional instrument
Hooks, Tenaculum = Mucosal retraction for taking biopsy or manipulating vagina or cervix
Examination of the endocervical canal :
Small cotton –tipped applicators
Endocervical speculum
Endocervical curettage :
Kevorkian curette
Fine Novak curete (>1mm) for small canal

## Slide 13
Notes: Laxity , relaxation of vaginal wall
Surgical tray containing the most commonly used supplies for performing a colposcopy.

## Slide 14
Notes: similar

## Slide 15: Other Equipment
Electrocautery
Cryosurgery
LEEP
LASER
“Optional”

## Slide 17: Colposcopic Technique
History taken and general physical examination performed
Lithotomy
Inspection, palpation : Vulva
Digital exam. : Vagina and cervix
Speculum insertion

## Slide 19: Colposcopic Technique
Cervix and vagina are visualized in natural state or after application of the normal saline.
Acetic acid is applied.
Acetowhite effect
: Latent interval minimum of 40 sec (or more)
: Transient effect, require reapplication of acetic acid
Vascular patterns :
: Ideal time to examine = just as the acetic acid effect is beginning to recede with green filter
Notes: Dab more acetic in there

## Slide 20: Acetic acid applying

## Slide 22
Green filter

## Slide 23
Notes: apperant

## Slide 24: Colposcopic Technique
Lugol’s or Schiller’s iodine : Non specific
Partial stain in Traumatized, inflamed squamous epithelium
Good for outlining the margin, vaginal lesion
Best for lesions in atrophic epithelium
Disadvantage => Obscure fine vessel detail
Notes: Nonspecific condition
AW is not apparent
Final step

## Slide 25: Lugol’s iodine applying
Notes: Mustard yellow
Spice = เครื่องเทศ

## Slide 26
Colposcopically Directed Biopsy
Colposcopic Technique
Notes: apperant

## Slide 27: Colposcopic Technique
Hemostasis
Monsel’s solution
Silver nitrate
Electrocautery
Tampon

## Slide 28: Colposcopic Technique
15% = unsatisfactory colposcopy (Type 3 T-zone)
ECC recommended in unsatisfactory colposcopy or no lesion is observed
Helpful to detect multifocal disease or early adenocarcinoma
Some suggested Cytobrush may be substitute for ECC and may be more sensitive.

## Slide 31: Colposcopic Technique
At the conclusion of colposcopy
Record of findings
Tentative plan
Hand-drawn impression, done immediately
Parameter : size, location, satisfactory, impression, warning sign of invasion
Position of all biopsy sites

## Slide 32
PLANNING COLPOSCOPY CLINIC
Notes: Finally , I ‘ll talk about

## Slide 33: Workload of colposcopy clinic
Diagnostic colposcopy appointments
Follow up colposcopy appointments
Outpatients LLETZ or other treatments
Inpatients LLETZ or other treatments
Excisional cone biopsies or other surgery
Vulvar disease and vulvodynia (vulva clinic)

## Slide 34
Colposcopy , CDB , ECC
LLETZ
Cold-kinfe Conization
Cryotherapy
Laser vaporization
Excision ; vagina, vulva
Hysteroscopy
Vulvar biosy , vaginal biopsy
Fractional curettage, endometrial biopsy
Other ; TAH
Procedures associated with colposcopy clinic

## Slide 35: Colposcopy clinic

## Slide 37
To ensure that colposcopist practices to a standard and to be accountable for their practice.
Why to have a good planning and management of colposcopic clinic ?
Notes: Accountable รับผิดชอบ อธิบายได้

## Slide 38: Clinic : Requirement
Reception/appointment office
Computer terminal connecting with hospital system
Secretary’s office and main computer connecting to colposcopy rooms
Patient waiting area, toilet
Technical maintenance laboratory
Staff rest room
Seminar room
Utility room
Notes: The following is an overview of the major requirements clinics must meet in order to
become

## Slide 39
Colposcope
LEEP/LLETZ unit (Laser : optional)
Cryotherapy unit
Suction system
Smoke evacuator
Recording system (optional)
Computer (optional)
Life-saving set
Equipment
Notes: The following is an overview of the major requirements clinics must meet in order to
become

## Slide 40
Information system, Data collection
Medical record
Colposcopic documemtation report
Cytological/histopathological report
Minimum data set
Notes: Documentation of the patient’s history may be performed using some modification of a standard gynecological record

## Slide 41: Management of health care wastes in screening clinics
Dispose contaminated objects in a properly marked leak proof container

## Slide 42: Spaulding’s categorization of medical instrument
Class | Use | Processing
Critical , “C” | Enter sterile body site or vascular system | Decontamination, cleaning followed by sterilization
Semicritical, “SC” | Comes into contact with intact mucous membrane or non-intact skin | Decontamination, cleaning follwed by HLD
Non-critical, “NC” | Comes into contact with intact-skin | Decontamination, cleaning followed by ILD or LLD
HLD = high-level disinfection
ILD = intermediate-level disinfection
LLD = low-level disinfection
Sellors JW, Sankaranarayanan R : Colposcopy and treatment of CIN : A beginners’ Manual

## Slide 44
Instrument | Processing | Suggested Procedure
Speculum, biopsy forceps, endocervical curette, needle holder, toothed forceps, insulated speculum | Decontamination and cleaning followed by sterilization or HLD * | Autoclaving or disinfection with boiling water
Gloves | Decontamination and cleaning followed by sterilization | Autoclaving as wrapped packs
Cryoprobes | Decontamination and cleaning followed by HLD | Disinfection with 0.1% chlorine or 2% glutaraldehyde or 6% hydrogen peroxide
Colposcope, LEEP equipment, cryogun and regulator, cryo gas cylinder, examination table, trolley, tray | Intermediate or low-level disinfection | Wipe with 60-90% ethyl, isopropyl alcohol
* HLD : High-level disinfection
Sellors JW, Sankaranarayanan R : Colposcopy and treatment of CIN : A beginners’ Manual
A guide to processing instrument and materials used for colposcopy clinic

## Slide 45: The End

## Slide 46
THANK YOU

## Slide 47
Perform cervical biopsies, if necessary
–Biopsy posterior areas first
–A depth of 3 mm is adequate
–Biopsy area of the lesion with worst features and closest to SCJ, include the area with atypical vessels