## Slide 1
Introduction to
Colposcopy
instrumentation
procedure and maintenance
Sathone Boonlikit,MD
Assoc Prof.
Division of Gynecologic Oncology
Rajavithi Hospital , Medical College Rangsit University ,Thailand
Sep 4-5 2017
Notes: Good afternoon

## Slide 2
Introduction to colposcopy
Instrumentation
Procedure
Maintenance
Outline

## Slide 3
INTRODUCTION
to
COLPOSCOPY
Notes: relevant [ADJ] เข้าประเด็น

## Slide 4
Colposcopy
- An optimal mean of investigating women with abnormal cervical cytology or positive cervical screening test
- Triage , particularly those who have been identified through screening tests to be at potential risk for developing cancer
Aim : to identify HSIL for optimal treatment
Notes: It is generally accepted that it is unethical to introduce a screening program wihtout being able to offer the good diagnosic and treatment facilities.
Colposcopy Clinic services can help women if their Pap Test results are abnormal.

## Slide 5
Is a medical diagnostic procedure to examine an illuminated, magnified view of the cervix and the tissues of the vagina and vulva using colposcope.
Magnification
enlarge the normal view by 2-60 times
Colposcopy
Notes: Colposcopy is usually done in a doctor's office, and the procedure typically takes 10 to 20 minutes. You'll lie on your back on a table with your feet in supports, just as during a pelvic exam or Pap test.

## Slide 6
colposcope
Notes: Unlike a (monocular) telescope, binoculars give users a three-dimensional image: for nearer objects the two views, presented to each of the viewer's eyes fro
m slightly different viewpoints, produce a merged view with an impression of depth.
เตียงตรวจนารีเวช Gynecological Table

## Slide 7
Notes: The company manufactures a wide variety of
instruments.
Colposcopes are quite heavy and are either mounted
on floor pedestals with wheels, suspended from a fixed
ceiling mount, or fixed to the examination table or to
a wall, sometimes with a floating arm to allow for
easier adjustment of position.

## Slide 8
Notes: A specialized colposcope equipped with a camera is used in examining
Accessories such as a monocular teaching side tube, photographic camera (Figure 4.2) and CCD video camera may be added to some colposcopes. However, these substantially increase the cost of the equipment.

## Slide 9
The Objectives of Colposcopy
2. To detect high grade lesion
(CIN 2/3, HSIL)
3. To guide appropriate treatment
1. To exclude invasive cancer
(for “triage”)

## Slide 10: Indications for colposcopy
Abnormal cytology LSIL/HSIL/Invasive/AGC (ASC-US+/-)
Abnormal-looking cervix
Persistent unsatisfactory cytology
Unsatisfactory cytology with positive of HR-HPV (in age≥ 30, cotest, optional)
Abnormal repeated cotest in cyto-/HPV +
Positive HPV genotyping 16/18
Positive of VIA , VILI
Case positive VIA/HPV and ineligible for cryotherapy
Abnormal screening test in post treatment case
Notes: remember, See also: bear in mind, keep in mind, recall

## Slide 11
Relative Contraindication
Active, inflammatory cervicitis
Heavy menses
Postmenopausal patient who is not estrogen-primed
Non-cooperative patient

## Slide 12
INSTRUMENTATIONS
OF
COLPOSCOPY
Notes: Let’s move on to the ………….

## Slide 13: Intrumentation
Colposcope
Equipment for examination
Biopsy Forceps
Additional instrument
Other equipment
Notes: Dedicated instrument

## Slide 14
Main objective Lens
Magnification changer
Eye pieces
Fine focus adjustment
Colposcope
Handle
Green filter
Notes: roughly, briefly

## Slide 15
OBJECTIVE LENS
- focal length 250-300 mm.
- working distance
Focal point
Image
Object
Object distance
Notes: blurred [ADJ] ซึ่งพร่ามัว
blur Distant things look blurred.
blur Close things look blurred
picture was blurred.
Focusing the colposcope is accomplished by adjusting the distance between the objective lens and the woman by positioning the instrument at the right working distance.
Colposcopes usually have fine focus adjustments so that, if the distance between the base of the scope and the woman is kept fixed, the focus of the scope may be altered slightly using the fine focusing handle.
The working distance (focal length) between the objective lens and the patient is quite important - if it is too long (greater than 300 mm) it is hard for the colposcopist’s arms to reach the woman, and if it is too short (less than 200 mm), it may be difficult to use instruments like biopsy forceps while visualizing the target with the scope. A focal distance of 250 to 300 mm is usually adequate.

## Slide 16: Equipment for examination
Examination table
Speculum
Cotton-tipped applicator & cotton swabs
Packing forceps
Sponge forceps
Solution’s container
Others

## Slide 17: Speculum
Variety sizes
Nonrefelctive matt surface : for laser and photography
Insulated, vinyl coated : for Leep
Tube for evacuate plume
Autoclavable

## Slide 18
Notes: They are made in a variety of sizes

## Slide 19
Speculum with smoke evacuation

## Slide 20
Normal saline
3-5 % acetic acid solution
Iodine solution -Schiller’s or Lugol’s
Monsel’s solution -ferric subsulfate
SOLUTIONS

## Slide 21
Acetic acid solution
Iodine solution -Schiller’s or Lugol’s

## Slide 22
SILVER NITRATE STICK
Monsel Solution

## Slide 23: Biopsy Forceps
Ideally, rectangular specimen
Teeth on jaws prevent slipping during biopsy
Spring handle => better cutting

## Slide 24: Biopsy forceps

## Slide 26: Additional instrument
Hooks, Tenaculum = Mucosal retraction for taking biopsy or manipulating vagina or cervix
Examination of the endocervical canal :
Small cotton –tipped applicators
Endocervical speculum
Endocervical curettage :
Kevorkian curette
Fine Novak curete (>1mm) for small canal
Notes: pull

## Slide 27: Endocervical Curette

## Slide 28: Additional instrument

## Slide 29
Endocervical Speculums

## Slide 30
Notes: Surgical tray containing the most commonly used supplies for performing a colposcopy.

## Slide 34: Other Equipment
Electrocautery
Cryosurgery
LEEP
LASER
“Optional”

## Slide 35
PROCEDURE

## Slide 36: Colposcopic Technique
Time to examination => Post menstrual period
Notes: Gap

## Slide 37: Colposcopic Technique
History taken and general physical examination performed
Lithotomy
Inspection, palpation : Vulva
Digital exam. : Vagina and cervix
Speculum insertion
Notes: Your doctor positions the special magnifying instrument, called a colposcope, a few inches away from your vulva. A bright light is shined into your vagina, and your doctor looks through the lens, as if using binoculars.

## Slide 39
Notes: A speculum is inserted into the vagina while examining the perineum, vulva, vagina, and cervix for lesions using the colposcope's white light and magnification

## Slide 41: Colposcopic Technique
Cervix are visualized in natural state or after application of the normal saline.
Acetic acid is applied.
Acetowhite effect
: Latent interval minimum of 40 sec (or more)
: Transient effect, require reapplication
Notes: Vascular patterns :
: Ideal time to examine = just as the acetic acid effect is beginning to recede, using light source or green filter

## Slide 42: Acetic acid applying
Notes: Dilute acetic acid is used to enhance any epithelial findings. It is applied to the entire cervix, causing abnormal tissue and some normal tissue to turn white.

## Slide 43
Notes: intermittently, periodically,

## Slide 44
Notes: Under white light, the cervix is visualized for acetowhite changes.

## Slide 45
Green filter
Notes: The green filter enhances visualization of blood vessels by making them appear darker in contrast to the surrounding epithelium.

## Slide 47: Colposcopic Technique
Lugol’s or Schiller’s iodine : Non specific
Partial stain in Traumatized, inflamed squamous epithelium
Good for outlining the margin, vaginal lesion
Best for lesions in atrophic epithelium
Disadvantage => Obscure fine vessel detail

## Slide 48: Lugol’s iodine applying
Notes: The principle behind the iodine test is that original and newly formed mature squamous metaplastic epithelium is glycogenated,
Columnar epithelium does not take up iodine and remains unstained, but may look slightly discoloured due to a thin film of iodine solution;
We recommend the routine use of iodine application in colposcopic practice as this may help in identifying lesions overlooked during examination with saline and acetic acid
and will help in delineating the anatomical extent of abnormal areas much more clearly, thereby facilitating treatment.

## Slide 49
Colposcopically Directed Biopsy
Colposcopic Technique
Notes: apperant

## Slide 50: Colposcopic Technique
Hemostasis
Monsel’s solution
Silver nitrate
Electrocautery
Tampon

## Slide 51: Taking Biopsy with Hemostasis

## Slide 52: Colposcopic Technique
15% unsatisfactory colposcopy
ECC recommended in unsatisfactory colposcopy or no lesion is observed
Helpful to detect multifocal disease or early adenocarcinoma
Some suggested Cytobrush may be substitute for ECC and may be more sensitive.

## Slide 54: Colposcopic Technique
At the conclusion of colposcopy
Record of findings
Tentative plan
Hand-drawn impression, done immediately
Parameter : size, location, satisfactory, impression, warning sign of invasion
Position of all biopsy sites
Notes: Documentation of the patient’s history may be performed using some modification of a standard gynecological record
Diagrammatic representations of the cervical , vaginal and vulva outlines with the anal region included, in the form of “blank” for drawing.

## Slide 55
Notes: Simplest method for documenting colposcopic findings
Diagrams may be drawn on printed outlines of the cervix
Cross-hatching = การแรเงา

## Slide 56
Post-Procedure Instructions

## Slide 57
MAINTENANCE

## Slide 58: Colposcopy clinic

## Slide 59: Workload of colposcopy clinic
Diagnostic colposcopy appointments
Follow up colposcopy appointments
Outpatients LLETZ or other treatments
Inpatients LLETZ or other treatments
Excisional cone biopsies or other surgery
Vulvar disease and vulvodynia (vulva clinic)

## Slide 60
Colposcopy , CDB , ECC
LLETZ
Cold-kinfe Conization
Cryotherapy
Laser vaporization
Excision ; vagina, vulva
Hysteroscopy
Vulvar biosy , vaginal biopsy
Fractional curettage, endometrial biopsy
Other ; TAH
Procedures associated with colposcopy clinic

## Slide 61
Processing of used instruments
Notes: A thorough knowledge and
understanding of the steps in the high-level disinfection
(HLD)/sterilization process is absolutely essential, as it
ensures that the instruments used are free of infectious
agents. Any lack of compliance with this process can
lead to contamination of the sterilized instruments and
harm to the patient.

## Slide 62: Methods of processing instruments
Decontamination
Cleaning
Sterilization / High-level disinfection
Storage
Handling
Notes: The process for re-use of the
instruments begins with decontamination and
continues through cleaning, sterilization/HLD, storage
and handling. A quality assurance programme will help
to ensure that instruments are processed adequately
for re-use.

## Slide 63: Spaulding’s categorization of medical instrument
Class | Use | Processing
Critical , “C” | Enter sterile body site or vascular system | Decontamination, cleaning followed by sterilization
Semicritical, “SC” | Comes into contact with intact mucous membrane or non-intact skin | Decontamination, cleaning follwed by HLD
Non-critical, “NC” | Comes into contact with intact-skin | Decontamination, cleaning followed by ILD or LLD
HLD = high-level disinfection
ILD = intermediate-level disinfection
LLD = low-level disinfection
Sellors JW, Sankaranarayanan R : Colposcopy and treatment of CIN : A beginners’ Manual

## Slide 64
Notes: Diagram

## Slide 65
Instrument | Processing | Suggested Procedure
Speculum, biopsy forceps, endocervical curette, needle holder, toothed forceps, insulated speculum | Decontamination and cleaning followed by sterilization or HLD * | Autoclaving or disinfection with boiling water
Gloves | Decontamination and cleaning followed by sterilization | Autoclaving as wrapped packs
Cryoprobes | Decontamination and cleaning followed by HLD | Disinfection with 0.1% chlorine or 2% glutaraldehyde or 6% hydrogen peroxide
Colposcope, LEEP equipment, cryogun and regulator, cryo gas cylinder, examination table, trolley, tray | Intermediate or low-level disinfection | Wipe with 60-90% ethyl, isopropyl alcohol
* HLD : High-level disinfection
Sellors JW, Sankaranarayanan R : Colposcopy and treatment of CIN : A beginners’ Manual
A guide to processing instrument and materials used for colposcopy clinic
Notes: Procedure tables, trolleys, equipment (colposcope,
cryosurgical equipment, electrosurgical generator,
smoke evacuator, halogen lamp, etc.) in the screening
clinic may be contaminated with body fluids such as
vaginal secretions, purulent discharge, blood, etc. While
the surface of the procedure table should be
decontaminated after each patient procedure, the other
surfaces should be decontaminated on a daily basis by
wiping with 0.5% chlorine solution, 60-90% ethyl or
isopropyl alcohol or other chemical disinfectants such as
iodophors. The floor of the screening clinic should also
be decontaminated on a daily basis.

## Slide 66: The End
Notes: I wish you all a successful seminar and a pleasant stay in Thailand. สวัสดีครับ

## Slide 67
THANK YOU